## Slide 1: ISI Space Antenna Results
Gabriel Burdan – 4/13/2026

## Slide 2: Quadrupole Turnstile Antenna
Current ISI Space Antenna configuration
Tuned to be impedance matched at 401 MHz
3U Structure underneath antenna
Fed with 4x lumped ports, each with a 90 degree phase offset

## Slide 3: 3D Gain Patterns

## Slide 4: 2D RHCP Gain Cuts @401 MHz
Good pattern symmetry within HPBW
Peak RHCP Gain = 3.71 dB
HPBW ~= 100 degrees
Main lobe orientation shown below

## Slide 5: 2D LHCP Gain Cuts @401 MHz
Good pattern symmetry within HPBW
Peak LHCP Gain = 2.21 dB
HPBW ~= 100 degrees
Main lobe orientation shown below

## Slide 6: Off Axis RHCP Radiation Properties
Pattern symmetry degrades away from boresight
RHCP Radiation for +/- 90 degrees off boresight shown
AR shown on next slide

## Slide 7: Axial Ratio @401 MHz
Main beams (RHCP and LHCP) have low AR
RHCP circularly polarized beamwidth ~= 64 degrees
LHCP circularly polarized beamwidth ~= 62 degrees
Off-axis EM waves linearly polarized

## Slide 8: Dipole Turnstile Antenna
Proposed ISI Space Antenna configuration
Tuned to be impedance matched at 401 MHz
3U Structure underneath antenna
Fed with 2x lumped ports, each with a 180 degree phase offset

## Slide 9: 3D Gain Pattern

## Slide 10: 2D Radiation Pattern
Linearly polarized omnidirectional pattern
Nulls at dipole ends (phi = 90 deg, theta ~= 90, 270 deg)
Peak gain = 3.63 dB

## Slide 11: Comparison to ISI Space Antenna Manual
Total dB Gain vs Theta @ Phi = 90
@ 401 MHz with 3U CubeSat Underneath
Total dB Gain vs Theta @ Phi = 0 (blue dotted line) for a UHF Antenna with 2U CubeSat Underneath
*Red arrows indicate direction CubeSat structure is pointing for each simulation
Omnidirectional pattern for both models
Peak gain aligned with CubeSat in both cases
Nulls at dipole ends (more on next slide)

## Slide 12: Comparison to ISI Space Antenna Manual
Total dB Gain vs Phi @ Theta = 90
@ 401 MHz with 3U CubeSat Underneath
Total dB Gain vs Phi @ Theta = 0 (solid red line) for a UHF Antenna with 2U CubeSat Underneath
Similar pattern asymmetry
Different coordinate axis definitions, but null observed in both patterns

## Slide 13: Next Steps
Model reflected power into antenna feeds inside TVAC chamber
Minimize reflected power using optimization