## Slide 1
SCT test tiers
What each tier adds to the loop
Ground side
Flatsat
SCT-1
Hydra
CDH
Hardwired
SCT-2
Hydra
GNU Radio
SDR
Li-2
CDH
Hardline RF
SCT-3
Hydra
GNU Radio
SDR
GS antenna
Antenna
Li-2
CDH
Short range
SCT-4
Hydra
GNU Radio
SDR
GS antenna
Antenna
Li-2
CDH
Long range
New in this tier
Solid: cabled link Dashed: over the air

## Slide 2
MCT: Hydra to CDH to Li-2 over UART
Verifies commands from Hydra reach the Li-2 through CDH and are acknowledged
Ground side
Flatsat
Hydra
Sends commands
CDH
Li-2
Command
Acknowledgment
Hardwired UART
UART
Logic analyzer
Checks no-op, transmit, reset
Commands reach the Li-2 over UART only, with no RF link to the ground side.
Built up one interface at a time: Hydra straight to the Li-2 first, then with CDH in the loop.

## Slide 3
SCT-1: Hardwired CDH and Hydra
Verifies CDH reads Hydra’s command bytes and Hydra reads CDH’s telemetry bytes, with no wireless link
Ground side
Flatsat
Hydra
Sends command, shows telemetry
CDH
CDH terminal
Verify command received
1. Command: housekeeping request
3. Telemetry: housekeeping packet
2.
Hardwired link, no RF

## Slide 4
SCT-2: Full chain, antenna out of the loop
Verifies a message can be sent in both directions through the hardware and software
Ground side
Flatsat
Hydra
GNU Radio
SDR
Li-2
CDH
Hardline RF
cabled, attenuated
Commands flow left to right, from Hydra to CDH. Telemetry flows right to left.
No antennas: the SDR and Li-2 are connected by cable.

## Slide 5
SCT-3: Antenna in the loop, short range
Verifies antenna and ground station performance and the ability to close the link
COSGC Ground Station
SWARM-EX Hydra and GNU Radio instances
Flatsat
Parking garage across from the DLC
Hydra
GNU Radio
SDR
GS antenna
Antenna
Li-2
CDH
Over the air
short range
Same flow as SCT-2, with both antennas added and the link closed over the air.

## Slide 6
SCT-4: Antenna in the loop, long range
Verifies antenna and ground station performance and closing the link over a longer range
COSGC Ground Station
SWARM-EX Hydra and GNU Radio instances
Flatsat
Farther from the ground station
Hydra
GNU Radio
SDR
GS antenna
Antenna
Li-2
CDH
Over the air
long range
Identical to SCT-3. Only the distance between the flatsat and the ground station changes.